## Slide 1
Kinecsterel
CS-308 Lab Project
Team:1
Nitant Vaidya 09005007
Priyank Parikh 09005006
Lalit Swami 09005028
Smit Patel 09005002

## Slide 2
Problem Statement
Aim to establish a Kinect-Esterel interface to control bot movements using hand gestures.
Captured gestures are transmitted wirelessly to the bot, where esterel takes the gesture input and generates appropriate signals.
Control the bot’s motions so that it can play football with another bot.
Both bots are independently controlled by two players using the same Kinect

## Slide 3
Requirements/Task Specifications
Capturing/Identifying gestures using Kinect
Transmitting them wirelessly to the bot
Esterel code which has support for ZigBee as input and generates appropriate signals based on received input
Defining actions for the bot based on these signals

## Slide 4
Project Plan
Wrote and debugged C# code for capturing gestures.
Independently tested gesture capturing by creating UI to print gestures. Verified that the chosen set of gestures are being identified correctly
Added zigbee support in esterel
Added a signal processing routine
Added Zigbee as an input signal
Tested using X-CTU
Step-by-Step Approach

## Slide 5
Project Plan
Tried to import a Zigbee module in C#. It didn’t work even after much effort and help from TAs. Hence Serial Port communication to transmit from C# code over Module to bot
Independently tested the Esterel input processing ability by manually sending bytes over Zigbee module
Added support for two players and modified UI accordingly.
Added support for automatically switching between one player and two player modes
Step-by-Step Approach

## Slide 6
Project Plan
Gesture capturing and transmission
Priyank Parikh and Lalit Swami
Esterel code and zigbee support in esterel
Nitant Vaidya and Smit Patel
Work-Division

## Slide 7
Project Plan
Gesture Capturing – 22nd March
Esterel Code – 4th April
Esterel Zigbee support – 5th April
Transmission – 8th April
Deadlines

## Slide 8
FSM
States and description
State: 1 – Forward
State: 2 – Hard Right
State: 3 – Hard Left
State: 4 - Reverse
State: 5 – Right
State: 6 – Left
State: 7 – Stop

## Slide 9
FSM
There is a global variable called gesture which stores the signal received over the zigbee moduele
On receipt of the signal, interrupt processing routine is called which changes the value of this variable, thereby causing the state transition
On receipt of input signal x next state becomes state x irrespective of current state, and the value of the variable is set to the character corresponding to that state

## Slide 10
Innovation and Challenges
Adding the “ZigBee wireless input as any input signal” abstraction in esterel
Deciding suitable gestures to make control easy, and writing code to recognize them. Ensuring a gesture isn’t a part of another gesture and can’t be interpreted as another gesture written above it (in the code)
Most challenging Aspects

## Slide 11
How they were tackled
Set the value of a global variable as a part of an interrupt processing routine. This variable’s value was what was returned to esterel when it would ask for the gesture value. When the gesture is read, the gesture code is wirelessly transmitted to the bot and the value of the global variable is updated. Added “ZigBee” as an input signal in the buildhash.pl file and wrote appropriate action for it.
Learned how to code gestures and ensured the more complicated gestures are defined first so that there is no interference

## Slide 12
Testing
The different modules of the project were independently tested before communication was established and the final testing was done
Gesture recognition was first verified by printing out the gesture name and gesture code as the operator made the gestures
Esterel code was debugged and tested by sending signals using X-CTU. We also tried many sending signals in quick succession to see if the bot responded quickly enough, and we found that it did
Testing of the combined modules was done using different people as operators whose gestures are to be captured. We also did two player testing, and checked if one’s gestures are interfering with another’s bot, and we found all of the above criteria to our satisfaction

## Slide 13
Performance Metrics
Delay: This was found to be really low, response time of the gesture recognition code as well as the gesture transmission time was found to be negligible and hence the bot was found to be very receptive to the incoming gesture
Degrees of freedom: As of now, the Firebird can have 7 states of motion. Forward, Backward, Hard Right, Hard Left, Right, Left, and Stop with the possibility of an easy increase to more states in the future.

## Slide 14
Abstraction and Re-usability
Since the code has been written in a modular fashion, a high level of abstraction is achieved
Esterel - Zigbee
Owing to the addition of ZigBee support in Esterel by including an input signal, any wireless input can be used by esterel code as input on the bot and appropriate esterel output signals can be generated as per requirement
Esterel code on any system besides the bot can also do the same

## Slide 15
Kinect Zigbee
The gesture recognition code can be used to transmit wirelessly to any other bot and any other system which uses Zigbee for input
Esterel code for an entirely different architecture can be written which uses the exact same gesture recognition code for input
Hence modularity led to a high level of abstraction and future usability

## Slide 16
Future Extentions
A project which aims to a bot which has esterel support, can control it using hand gestures by only assigning appropriate esterel signals for different actions
A project which wishes to control the bot wirelessly (using gestures or without) can do so by only sending the input signal via the ZigBee module
A project which wishes to use Kinect hand gestures for any purpose whatsoever could use our predefined code to simply call functions on capturing appropriate gestures

## Slide 17
Examples:
An air-freshener bot which receives input from various sensors of odour levels in a house wirelessly and performs air freshening action if odour levels are too high in any particular area.
A mechanical arm which is controlled by Kinect gestures and coded using Esterel. It can mimic hand actions allowing for better control and be used in locations inaccessible to the human hand.

## Slide 18
Future Enhancements
Better Control
Currently there are 7 gestures : Right, Left, Hard Right, Hard Left and other motions.
There is scope to increase the detail of this motion and make it move left or right by a certain degrees based on the angle of tilt of the hand. This allows for much better bot control
This would be more useful from a football playing perspective since a high measure of control is desired

## Slide 19
Using Zigbee Channels
Currently we are using two different Zigbee chips to transmit independently to two different bots
A possible enhancement is to use different channels on single chip to transmit to two bots
This might cause a little delay but that would be negligible. It would reduce hardware requirements and also the need to configure the extra zigbee module

## Slide 20
Vote of thanks
We would like to thank the ERTS lab team and the TAs for helping and guiding us throughout the duration of project